## Slide 1: Optimizing Multi-Layer Radiation Absorbing Materials: Advanced Algorithmic Solutions
Joey Antonucci, Tegan Carr, Abegale Jones
Sponsored by
Faculty: Dr. Paul Leu, Dr. Jungtaek Kim, Mr. Mingxuan Li
DEVCOM: Dr. Quang Nguyen

## Slide 2
Radiation-absorbing coatings are more than just a tool for stealth—they’re a gateway to a smarter, safer, and more efficient future.

## Slide 3: Radiation Absorbing Material Coatings are Widely Used in a Variety of Military and Civil Applications
Military Applications:
Aircraft
  Stealth fighters, bombers
Missiles
  Cruise and ballistic missiles
Ground Vehicles
  Tanks and armored vehicles
Naval Vessels
  Surface ships, submarines
Satellites
Wikipedia contributors. (2024, November 29). Lockheed Martin F35 A.

## Slide 4: Radiation Absorbing Material Coatings are Widely Used in a Variety of Military and Civil Applications
Civil Applications:
Telecommunications
  Signal management
Automotive Industry
  Electric vehicles
Architecture and Construction
  Energy efficiency
Consumer Electronics
  Smartphones, laptops, tablets
DeepCoat. (n.d.). How EMI shielding protects cell phones. DeepCoat. Retrieved November 29, 2024

## Slide 5: Radiation Absorbing Materials Minimize Radar Detection by Converting Electromagnetic Waves into Heat or Destructive Interference
Wang, X. (2024). Radar absorbing material. Radar Absorbing Material - an overview | ScienceDirect Topics. https://www.sciencedirect.com/topics/materials-science/radar-absorbing-material
Notes: RAM is designed to absorb incoming radar waves instead of reflecting them. This is achieved through materials that have specific electromagnetic properties, such as a high magnetic or dielectric loss, which convert the electromagnetic energy into heat.

## Slide 6: RAM Advancements use Nanomaterials, Optimized Structures, and Algorithm-driven Simulations to Enhance Absorption and Stealth Performance
Notes: The development of advanced RAM technology increasingly relies on computational tools and algorithms to optimize material composition and performance. Genetic algorithms, machine learning, and Bayesian optimization are employed to explore the vast design space of potential material combinations. These methods simulate interactions between electromagnetic waves and materials, evaluating properties like dielectric constants, magnetic permeability, and layer thicknesses.

## Slide 7: Building on Existing Work: Advancing the Project Through Prior Foundations
Existing Python Codebase in GitHub
MATLAB Contributions by Sponsor
Published Research on Genetic Algorithms

## Slide 8: Objective: Optimize Mutli-Layer Radiation Absorbing Materials Using Algorithms

## Slide 9
Requirements
&
Specifications
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization
The Material Must be Thin and Easy to Manufacture
Maximum of 5 material thick
Total material thickness < 7 mm
Minimize Total Radar Reflection
Keep reflection of broad-band frequencies under –30 dB
Make a Template for ARL to Import Materials
Import 16 fictious materials
Create air and PEC layers surrounding material

## Slide 10
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material
Relative Permitivities and Permeabilities
of the Materials in the Database

## Slide 11
The Material Must be Thin and Easy to Manufacture
Maximum of 5 materials thick
Total material thickness < 7 mm

## Slide 12
Minimize Total Radar Reflection
Keep reflection of broad-band frequencies under –30 dB

## Slide 13
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization

## Slide 14: What is the Best Method to Optimize a Multi-Layer Radiation Absorbing Material?

## Slide 15: A Pugh Chart was Used to Down Select Design Criteria
Pugh Chart of Preliminary Designs:

## Slide 16: A Genetic Algorithm Mimics the Process of Natural Selection to Evolve Solutions
Natural Selection:
Genetic Algorithm:

## Slide 17: A Random Initial Population Allows for More Exploration of the Solution Space
1st Generation
Random
Population
of 4
1 Chromosome
0.10 2.56 4.89 1 14 13
3.45 1.32 0.78 4 8 15
2.17 2.01 1.64 5 12 9
3.00 0.24 0.74 2 10 2
Thickness
Material

## Slide 18: A Fitness Functio​n Guides the Algorithm Toward Selecting an Optimal Solution
1st Generation
Random
Population
of 4
1 Chromosome
0.10 2.56 4.89 1 14 13
3.45 1.32 0.78 4 8 15
2.17 2.01 1.64 5 12 9
3.00 0.24 0.74 2 10 2
Thickness
Material
R = -20.45 [dB]
R = -31.01 [dB]
R = -30.30 [dB]
R = -27.19 [dB]

## Slide 19: Crossover and Mutation Allow the Solution to Evolve Over Generations
2nd Generation
Random
Population
of 4
1 Chromosome
0.10 2.56 4.89 1 8 13
3.45 1.32 0.78 4 14 15
2.17 2.01 1.64 5 12 9
3.00 0.24 0.74 2 10 2
Thickness
Material
R = -19.82 [dB]
R = -36.90 [dB]
R = -30.30 [dB]
R = -27.19 [dB]

## Slide 20: Crossover and Mutation Allow the Solution to Evolve Over Generations
2nd Generation
Random
Population
of 4
1 Chromosome
0.10 2.56 4.89 1 8 13
3.45 1.32 0.78 4 14 15
1.25 2.01 1.64 5 12 9
3.00 0.24 0.74 2 10 2
Thickness
Material
R = -19.82 [dB]
R = -36.90 [dB]
R = -21.10 [dB]
R = -27.19 [dB]

## Slide 21: Crossover and Mutation Allow the Solution to Evolve Over Generations
2nd Generation
Random
Population
of 4
1 Chromosome
0.10 2.56 4.89 1 8 13
3.45 1.32 0.78 4 14 15
1.25 2.01 1.64 5 12 9
3.00 0.24 0.74 2 10 2
Thickness
Material
R = -19.82 [dB]
R = -36.90 [dB]
R = -21.10 [dB]
R = -27.19 [dB]

## Slide 22: Genetic Algorithms Converge on an Optimal Solution

## Slide 23: Results are Validated by Comparing Values to Proven MATLAB Code
Genetic Algorithm Results
Proven MATLAB Results

## Slide 24: Overlaying Data from Multiple Layers Allows us to Compare Results
2 Layer:
t = [3.25 0.26] (mm)
M = [4 6]
R = -21.13 (dB)
3 Layer:
t = [3.81 1.39 1.46] (mm)
M = [4 8 15]
R = -37.10 (dB)
4 Layer:
t = [3.81 0.15 1.42 1.44] (mm)
M = [4 15 8 15]
R = -36.46 (dB)
5 Layer:
t = [3.58 1.61 0.78 0.67 0.24] (mm)
M = [4 8 15 16 4]
R = -37.28 (dB)

## Slide 25: Total Thickness Also Plays a Role in Optimal Reflection Values

## Slide 26: Bayesian Optimization: Enhancing Solutions Through Informed Search
Probabilistic Model
Use of Acquisition Function to Balance of Exploration and Exploitation

## Slide 27: Genetic Algorithm vs Bayesian Optimization
 | GA | Bayesian
Average Run Time | 1.01 (minute) | 70.42 (minutes)
Number of Runs | 10 | 10
Number of Evaluations per Run | 1010 | 1010
Optimal Solution | -20.82 (dB) | -22.36 (dB)

## Slide 28: Genetic Algorithm vs Bayesian Optimization
 | GA | Bayesian
Average Run Time | 1.01 (minute) | 70.42 (minutes)
Number of Runs | 10 | 10
Number of Evaluations per Run | 1010 | 1010
Optimal Solution | -20.82 (dB) | -22.36 (dB)

## Slide 29: Genetic Algorithm vs Bayesian Optimization
 | GA | Bayesian
Average Run Time | 1.01 (minute) | 70.42 (minutes)
Number of Runs | 10 | 10
Number of Evaluations per Run | 1010 | 1010
Optimal Solution | -20.82 (dB) | -22.36 (dB)

## Slide 30: Comparing the Results for Bayesian Optimization and Genetic Algorithm
Genetic Algorithm:
Bayesian Optimization:

## Slide 31
Requirements
&
Specifications
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization
The Material Must be Thin and Easy to Manufacture
Maximum of 5 materials thick
Total material thickness < 7 mm
Minimize Total Radar Reflection
Keep reflection of broad-band frequencies under –30 dB
Make a Template for ARL to Import Materials
Import 16 fictious materials
Create air and PEC layers surrounding material

## Slide 32
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material

## Slide 33
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material

## Slide 34
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material
Given:
Relative Permeability (μ)
Relative Permittivity (ε)

## Slide 35
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material
Given:
Relative Permeability (μ)
Relative Permittivity (ε)
Calculate:
Refractive Index (n)
Extinction Coefficient (k)

## Slide 36
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material
Given:
Relative Permeability (μ)
Relative Permittivity (ε)
Calculate:
Refractive Index (n)
Extinction Coefficient (k)

## Slide 37
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material
Given:
Relative Permeability (μ)
Relative Permittivity (ε)
Calculate:
Refractive Index (n)
Extinction Coefficient (k)
Create csv file for each material:
[nm]
[-]

## Slide 38
Make a Template for ARL to Import
Materials
Import 16 fictious materials
Create air and PEC layers surrounding material
Air:
n = 1
k = 0
PEC:
n = 0
k = ∞
Integrated into the codebase

## Slide 39
The Material Must be Thin and Easy to Manufacture
Maximum of 5 materials thick
Total material thickness < 7 mm

## Slide 40
The Material Must be Thin and Easy to Manufacture
Maximum of 5 materials thick
Total material thickness < 7 mm
2 Layer:
t = 3.51 [mm]
4 Layer:
t = 6.82 [mm]
5 Layer:
t = 6.88 [mm]
3 Layer:
t = 6.66 [mm]

## Slide 41
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization

## Slide 42
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization
MATLAB Run Time:
Non-Vectorized: 11.24 (sec)
Vectorized: 2.46 (sec)

## Slide 43
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization

## Slide 44
Efficiently Execute
MATLAB & Python Scripts
Vectorize FOR Loops
Genetic Algorithm (GA)
Bayesian Optimization

## Slide 45
Minimize Total Radar Reflection
Keep reflection of broad-band frequencies under –30 dB

## Slide 46
Minimize Total Radar Reflection
Keep reflection of broad-band frequencies under –30 dB
2 Layer:
R = -21.13 (dB)
4 Layer:
R = -36.46 (dB)
5 Layer:
R = -37.28 (dB)
3 Layer:
R = -37.10 (dB)

## Slide 47: Semester Summary: Highlights and Insights
Budget: 72.69 (seconds) to Run Code at 100 populations and 100 generations
Engineer Cost per Hour: $150
$3 per run

## Slide 48: The Work Done in MATLAB Will Be Transferred to Python
Transition to Python
  Recreate genetic algorithm, Bayesian Optimization in Python
Enhanced Functionality
  Incorporate machine learning and deep learning models.
Improved Efficiency
  Optimize code to run faster with larger data sets
Scalability
  Further develop material database
Real-World Testing
  Create physical models of material layers

## Slide 49: Sources:
[1.] Michielssen, E., et al. “Design of lightweight, broad-band microwave absorbers using genetic algorithms.” IEEE Transactions on Microwave Theory and Techniques, vol. 41, no. 6, 1993, pp. 1024–1031, https://doi.org/10.1109/22.238519.
[2.] Kilic, Ozlem, and Q. M. Nguyen. “Application of artificial immune system algorithm to electromagnetics problems.” Progress In Electromagnetics Research B, vol. 20, 2010, pp. 1–17, https://doi.org/10.2528/pierb10010701.